ECE R48 INSTALLATION OF LIGHTS 04-S9 2012/11/18 燈光信號裝置安裝
增/修內容	原內容	修訂國內法規條文草案	對應國內法規條文
2. DEFINITIONS / ... / 2.7.31. "Manoeuvring lamp" means a lamp used to provide supplementary illumination to the side of the vehicle to assist during slow manoeuvres.	2. DEFINITIONS / ...	三之三、車輛燈光與標誌檢驗規定：自一０二年一月一日起實施 / 三之四、車輛燈光與標誌檢驗規定：自一０六年一月一日起實施 / 2.28 低速輔助照明燈(Manoeuvring lamp)：係指當車輛低速行駛時，用於提供車輛側方輔助照明光度之燈具。	三之三、車輛燈光與標誌檢驗規定：自一０二年一月一日起實施 / 三之四、車輛燈光與標誌檢驗規定：自一０六年一月一日起實施
6.19.7.4. The lamps referred to in paragraph 5.11. may be switched ON when the daytime running lamps are switched ON, except if daytime running lamps are operating according to paragraph 6.2.7.6.2., where at least the rear position lamps shall be activated.	6.19.7.4. The lamps referred to in paragraph 5.11. are not switched ON when the daytime running lamps are switched ON, except if daytime running lamps are operating according to paragraph 6.2.7.6.2.	6. 車輛因行車安全或特定操作之需，得裝置符合下列規定之輔助燈光與標誌。 / 6.3 汽車晝行燈(daytime running lamp)： / ... / 6.3.6 電路接線： / ... / 6.3.6.4 當開啟晝行燈時，其4.23所述之燈具不能可被點亮，惟若晝行燈係依照4.2.6.6.2之規定操作時，其應至少點亮尾燈。	6. 車輛因行車安全或特定操作之需，得裝置符合下列規定之輔助燈光與標誌。 / 6.3 汽車晝行燈(daytime running lamp)： / ... / 6.3.6 電路接線： / ... / 6.3.6.4 當開啟晝行燈時，其4.23所述之燈具應不能被點亮，惟若晝行燈係依照4.2.6.6.2之規定操作時則除外。
5. GENERAL SPECIFICATIONS / ... / 5.15. The colours of the light emitted by the lamps7 are the following: / ... / Adaptive front- lighting systems (AFS): white. / Exterior courtesy lamp: white. / Manoeuvring lamp: white.	5. GENERAL SPECIFICATIONS / ... / 5.15. The colours of the light emitted by the lamps7 are the following: / ... / Adaptive front-lighting systems (AFS): White / Exterior courtesy lamp: White
6. INDIVIDUAL SPECIFICATIONS / ... / 6.26. Manoeuvring lamps (Regulation No. 23) / 6.26.1. Presence / Optional on motor vehicles. / 6.26.2. Number / One or two (one per side) / 6.26.3. Arrangement / No special requirement, however the requirements of paragraph 6.26.9. apply. / 6.26.4. Position / No special requirement. / 6.26.5. Geometric Visibility / No special requirement. / 6.26.6. Orientation / Downwards, however the requirements of paragraph 6.26.9. apply. / 6.26.7. Electrical Connections / Manoeuvring lamps shall be so connected that they cannot be activated unless the mainbeam headlamps or the dipped-beam headlamps are switched ON at the same time. / The manoeuvring lamp(s) shall be activated automatically for slow manoeuvres up to 10 km/h provided that one of the following conditions is fulfilled: / (a) Prior to the vehicle being set in motion for the first time after each manual activation of the propulsion system; or / (b) Reverse gear is engaged; or / (c) A camera based system which assists parking manoeuvres is activated / The manoeuvring lamps shall be automatically switched off if the forward speed of the vehicle exceeds 10 km/h and they shall remain switched off until the conditions for activation are met again. / 6.26.8. Tell-tale / No special requirement. / 6.26.9. Other requirements / 6.26.9.1. The Technical Service shall, to the satisfaction of the authority responsible for type approval, perform a visual test to verify that there is no direct visibility of the apparent surface of these lamps, if viewed by an observer moving on the boundary of a zone on a transverse plane 10 m from the front of the vehicle, a transverse plane 10 m from the rear of the vehicle , and two longitudinal planes 10 m from each side of the vehicle; these four planes to extend from 1 m to 3 m above and parallel to the ground as shown in Annex 13. / 6.26.9.2. At the request of the applicant and with the consent of the Technical Service the requirement of 6.26.9.1 may be verified by a drawing or simulation or deemed be satisfied if the installation conditions comply with paragraph 6.2.3 of Regulation No. 23, as noticed in the communication document in Annex 1, paragraph 9.	6. INDIVIDUAL SPECIFICATIONS / ... / 6.25.8. Tell-tale / Optional	6.22 低速輔助照明燈 / 6.22.1 燈色應為白色。 / 6.22.2 數量：一或二個(每側各一盞） / 6.22.3 燈具配置：應符合6.22.6 其他要求之規定。 / 6.22.4 投射方向：朝下。然而，其應符合6.22.6 其他要求之規定。 / 6.22.5 電路接線：低速輔助照明燈應於遠光頭燈或近光頭燈點亮時方能作動。 / 若車輛符合下列條件之一且車輛低速行駛未逾一０公里/小時時，則低速輔助照明燈應被自動點亮： / (a)在每次手動啟動推進系統後之車輛首次開始移動之前；或 / (b)變速箱檔位位於後退檔位；或 / (c)攝影機系統於輔助停車操作時被啟動。 / 當車輛往前行駛之速度逾十公里/小時，則低速輔助照明燈應自動熄滅，且其應持續保持熄滅，直到再次滿足啟動條件。 / 6.22.6：其他要求 / 6.22.6.1 檢測機構人員應進行目視檢測，以確認無法直接可視該燈之外表面；檢測時應分別自距離車輛前方、後方及兩側一０公尺之位置進行平行於車輛之移動與目視檢測，此四面向應與地面平行且自距地高一公尺延伸至三公尺，如圖七所示。 / 6.22.6.2 若低速輔助照明燈之安裝狀態符合本基準「低速輔助照明燈」4.2之規定時，經檢測機構同意後，前述規範亦可視為符合，或以圖說或模擬方式進行驗證。	無
Annex 13（經查ECE R23 並無6.2.3條文） / Observing area towards the apparent surface of manoeuvring lamps / (如下圖所示)	無	圖七 低速輔助照明燈外表面之觀察區域	無

Zones of observation 觀察區域
This drawing shows the zone from one side, the other zones are from the front, the rear and from the other side of the vehicle
顯示車輛之一側方區域，車輛之前方、後方區域及另一側方區域

三公尺
二公尺
一公尺
一０公尺
一０公尺

Boundaries of the zones區域邊界

一０公尺
一０公尺
一０公尺
一０公尺

        圖七