ECE R94(前方碰撞乘員保護)及ECE R95(側方碰撞乘員保護)
        （Draft proposal: ELSA-7-03 and ELSA-7-04）
ECE 條文	中文翻譯
2.6.7. The place of the RESS. / 2.7. “Compartment”means bounded zone in vehicle, / 2.7.1 Passenger compartment means the space for occupant accommodation, bounded by the roof, floor, side walls, doors, outside glazing and front bulkhead and the plane of the rear compartment bulkhead or the plane of the rear-seat back support, or rear gate, as well as by the barriers and enclosures provided for protecting the power train from direct contact with live parts. / 2.7.2. Luggage compartment means the space in the vehicle for luggage accommodation, bounded by the roof, hood, floor, side walls, as well as by the barrier and enclosure. For electric vehicles, hybrid vehicles and fuel cell vehicles the barrier and enclosure are provided for protecting the power train from direct contact with live parts, being separated from the passenger compartment by the front bulkhead or the rear bulk head,	2.6.7 充能系統的設置位置 / 2.7 乘室：指車內之乘員空間。 / 2.7.1 乘員之乘室：指使用者所使用之空間，受限於車輛之車頂、地板、側邊之車輛內壁、車門、外部玻璃及前端乘室壁和後端乘室壁之平面或後端坐倚靠背之平面，或後攔板，以及由屏障或外殼提供之保護無法於帶電體直接接觸動力裝置。 / 2.7.2 行李空間：指車輛裡的空間是用來置放行李，受限於車頂、車蓋、側邊之車輛內壁以及屏障或外殼。對電動車輛而言，油電混合車及燃料電池車的屏障和外殼之保護無法於帶電體直接接觸動力裝置，被分隔開來的乘客空間是由前端乘室壁和後端乘室壁所區隔的。
2.15. “Electric power train” means the electrical circuit which may include the RESS, the energy conversion system, the electronic converters, the traction motors, the associated wiring harness and connectors, and the coupling system for charging the RESS,	2.15 電力電動裝置：指電路應包含充能系統，能量轉換系統，電子整流器，牽引馬達和相關之電路線束、接頭和充能系統充電之耦合系統。
2.16. “RESS” means rechargeable energy storage system that provides the electric energy for propulsion,	2.16 充能系統：可再充電儲能系統提供電力能量來推進。
2.17. “Energy conversion system” means system that generates and provides electric energy for propulsion,	2.17能量轉換系統：指系統能產生和提供電能來推進。
2.18. “Electronic converter” means a device capable of controlling or converting electric power,	2.18 電子整流器：指此裝置能控制或轉換成電能。
2.19. “Coupling system for charging the RESS” means the electrical circuit used for / charging the RESS from an external electric power supply (AC or DC electric power supply outside of the vehicle) including the vehicle inlet,	2.19 充能系統充電之耦合系統：指充能系統使用外部電源供應器之電路來充電（車輛外交流或直流電之電源供應）
2.20. “Direct contact” means the contact of persons with live parts,	2.20 直接接觸：指人與帶電體之接觸。
2.21. “Live parts” means conductive part(s) intended to be electrically energized in normal use,	2.21 帶電體：指在一般正常使用下帶電之導體或可導電零件。
2.22. “Indirect contact” means the contact of persons with exposed conductive parts,	2.22間接接觸：指人與外露之可導電零件接觸。
2.23. “Protection degree” means Protection provided by a barrier/enclosure related to the contact with live parts by a test probe, such as a test finger (IPXXB), or a test wire (IPXXD),	2.23 防護等級：指由屏障/外殼所提供之保護是與試驗探棒接觸帶電體有關，比如測試棒 (IPXXB),或試驗線(IPXXD)。
2.24. “Exposed conductive part” means conductive part which can be touched, and which only becomes electrically energized under failure conditions,	2.24 外露導電元件：指導電元件可被碰觸，只有在電能產生失效的情況下。
2.25. “Electrical circuit” means an assembly of connected live parts which is designed to be electrically energized in normal operation,	2.25 電路：指由連接之帶電體所構成，在一般操作情況下可導通電流。
2.26. “Working voltage” means he highest value of an electrical circuit voltage, specified by the manufacturer, which may occur between any conductive parts in open circuit conditions or under normal operating conditions,	2.26工作電壓：指電子線路電壓的最高值，由製造廠具體說明，在短路的情況下或一般運作的情況下，也可能會產生的絕緣情況。
2.27. “Electrical chassis” means a set made of conductive parts electrically linked together, whose potential is taken as reference,	2.27電路介面：指由導電的元件所組成連結，其應參考其電位。
2.28. “Solid insulator” means insulating coating of wiring harnesses provided in order to cover and protect the live parts against direct contact from any direction of access; covers for insulating the live parts of connectors; and varnish or paint for the purpose of insulation,	2.28 固體絕緣體：指電路線束的絕緣外表提供為了要涵蓋和保護從任何方向直接碰觸到帶電體；涵蓋範圍為連接接頭之帶電體的絕緣，以絕緣漆或為了絕緣所塗上的。
2.29. “Barrier” means the part providing protection against direct contact to the live parts from any direction of access,	2.29 屏障：指此部件提供從任何方向直接接觸帶電體之防護措施。
2.30. “Enclosure” means the part enclosing the internal units and providing protection against direct contact from any direction of access,	2.30 外殼：指部件能容納內部之設備和提供從任何方向直接接觸之防護措施。
2.31. “High Voltage” means classification of an electric component or circuit, if its maximum working voltage is > 60 V and ≤ [1500] V d.c. or > 30 V and ≤ [1000] V a.c.	2.31 高電壓：指電子元件和電路的分類，假如它的最大工作電壓是> 60 V and ≤ [1500] V d.c. or > 30 V and ≤ [1000] V a.c.
2.32. “High Voltage Bus” means electrical circuit, including the coupling system for charging the RESS, that operates on high voltage	2.32 高電壓匯流排：指電路包含充能系統充電之耦合系統是在高電壓狀態下運作。
5.2.8. This requirements are apply to the electric power train of electric vehicles, hybrid vehicles and fuel cell vehicles, and the high voltage components and systems which are galvanically connected to the high voltage bus of the electric power train following vehicle crash test(s).	5.2.8 本規範適用於電動車、複合動力車輛、燃料電池車輛及與電力傳動系統之高電壓匯流排連接之高電壓零組件/系統，於碰撞測試後之規範。
5.2.8.1. Not more than 5.0 liters of electrolyte from propulsion batteries shall spill outside the passenger compartment, and no visible trace of electrolyte shall spill into the passenger compartment, within 30 minutes after a barrier impact test. / Compliance may be demonstrated by test or analysis.	5.2.8.1於執行完碰撞測試後30分鐘內，用來推進車輛之電池於乘室外不得洩漏超過5公升之電池液，且於乘室內不得有可見之電池液痕跡。另可以測試或分析方式確認其符合性。
5.2.8.2. Battery modules located inside the passenger compartment must remain in the / location in which they are installed. No part of any battery system component that is located outside the passenger compartment shall enter the passenger compartment during the test procedures, as determined by visual inspection.	5.2.8.2安裝於乘室內之電池模組須維持於其安裝之位置。並應以目視方式確認任何安裝於乘室外之電池系統未於測試過程中入侵乘室。
5.2.8.3. After the test, at least one of the following criteria specified in paragraph 5.2.8.3.1 thorough paragraph 5.2.8.3.4 shall be met. If the vehicle has an automatic disconnect function, the criteria shall be applied to each divided portion individually	5.2.8.3測試後應至少符合下列條文5.2.8.3.1至5.2.8.3.4。若車輛配備有自動斷電功能，該功能應能獨立運作於各個部分。
5.2.8.3.1. Isolation Resistance: If the electrical circuit divided by the disconnect function / includes AC circuit, this part of the high voltage bus shall be considered as an AC high voltage bus. If the electrical circuit divided by the disconnect function doesn't include AC circuit, this part of the high voltage bus shall be considered as a DC high voltage bus. / For AC high voltage buses, isolation resistance between the high voltage bus and the electrical chassis shall have minimum value of 500 ohms/volt of working voltage. If the protection degree IPXXB is satisfied for AC portion of the high voltage buses after crash, isolation resistance between the high voltage bus and the electrical chassis shall have minimum value of 100 ohms/volt of working voltage. / For DC high voltage buses, isolation resistance between any high voltage bus and the electrical chassis shall have minimum value of 100 ohms/volt of working voltage.	5.2.8.3.1絕緣電阻：若斷電功能包含AC電路，則該部分之高電壓匯流排應視為AC高電壓匯流排。若斷電功能未包含AC電路，則該部分之高電壓匯流排應視為DC高電壓匯流排。 / 對於AC高電壓匯流排：高電壓匯流排與電路介面(Electrical Chassis)間之絕緣電阻應有至少500ohms/volt之工作電壓。若撞擊測試後IPXXB等級之防護滿足AC方面之高電壓匯流排要求，則高電壓匯流排與電路介面間之絕緣電阻應有至少100ohms/volt之工作電壓。 / 對於DC高電壓匯流排：任何高電壓匯流排與電路介面間之絕緣電阻應至少有100ohms/volt之工作電壓。
5.2.8.3.2. Voltage: For AC high voltage buses, voltage of the bus shall be equal to or less than 30 VAC. For DC high voltage buses, voltage of the bus shall be equal to or less than 60 VDC	5.2.8.3.2電壓：對於AC高電壓匯流排，匯流排之電壓應等於或小於30VAC。對於DC高電壓匯流排者，則匯流排之電壓應等於或小於60VDC。
5.2.8.3.3. Energy: Energy on the high voltage bus shall be less than 0.2 Joules.	5.2.8.3.3能量：於高電壓匯流排處應小於0.2焦耳。
5.2.8.3.4. Physical Protection: For protection of live parts, the protection degree IPXXB shall be provided. / For protection against indirect contact with live parts, all exposed conductive parts electro shall be securely connected to the electrical chassis such that no dangerous potentials are produced. / The resistance between the electrical chassis and all conductive parts shall be less than 0.1 ohm, which is measured when there is a current flow of at least 0.2 amps. / The said resistance shall be regarded as lower than 0.1 ohm when it is clearly evident that the DC electrical connection has been established adequately and securely by welding.	5.2.8.3.4物理防護：應提供IPXXB等級之防護，以保護生物體。 / 為保護帶電體之間接接觸，所有外露具有傳導力的導體應確保連接至電路介面，以確保不會產生危險之可能。 / 電路介面與所有具傳導力導體間之電阻應小於0.1歐姆，此係以至少0.2安培之電流進行量測。 / 當可清楚顯示DC電子之連接係以適當且安全地方式焊接時，則所述之電阻應被視為小於0.1歐姆。
11. TRANSITIONAL PROVISIONS / 11.1. As from the official date of entry into force of Supplement 1 to the 01 series of amendments, no Contracting Party applying this Regulation shall refuse to grant ECE approval under this Regulation as amended by Supplement 1 to the 01 series of amendments. / 11.2. As from 1 October 2002, Contracting Parties applying this Regulation shall grant ECE approvals only to those types of vehicles which comply with the requirements of this Regulation as amended by Supplement 1 to the 01 series of amendments. / 11.3. As long as there are no requirements in this Regulation with regard to the protection of the occupants by means of a full frontal impact test, Contracting Parties may continue to apply the requirements already in force for that purpose at the time of acceding to this Regulation.	11.過渡條款 / 11.1 從01-S1系列修正版強制實施之日期起，所有導入此法規之締約方在此01-S1系列修正版之修正法規下不得拒絕ECE認證。 / 11.2 從2002年10月1日後，導入此法規之締約方應針對符合01-S1系列修正版規範之車輛型式進行ECE認證。 / 11.3 除非此項前方碰撞乘員保護法規未規範，否則締約方得持續符合在此法規已經強制實施之項目規範。
Annex 3 / TEST PROCEDURE / 1.4.4. Electric vehicle adjustments / 1.4.4.1. The high voltage system shall be energized. / 1.4.4.2. The RESS is at the level specified in the following paragraph (a), (b), or (c), as appropriate: / (a) At the maximum state of charge recommended by the manufacturer, as stated in the vehicle operator's manual or on a label that is permanently affixed to the vehicle; / (b) If the manufacturer has made no recommendation, at a state of charge of not less than 95 percent of the maximum capacity of the RESS; or / (c) If the RESS are rechargeable only by an energy source on the vehicle, at any state of charge within the normal operating voltage, as defined by the vehicle manufacturer. / 1.4.4.3. Energy conversion system: Proposal from OICA together with JASIC	附件三 測試程序 / 1.4.4電動車之調整 / 1.4.4.1高電壓系統應供電。 / 1.4.4.2 充能系統應適當的位於下述情形之一： / (a)充能至製造廠建議之最大狀況，如車主手冊或永久固定於車輛上之標記所述。 / (b)若製造廠無建議時，則應充能至不少於RESS最大容量95%之狀況；或 / (c)若RESS僅能由車輛之動力來源進行充能，則應充能至製造廠定義之正常操作電壓。 / 1.4.4.3能量轉換系統：(內容待定)
Annex 11 / ELECTRIC SAFETY – TEST PROCEDURES / This section describes test procedures. Alternative test and analysis methods may also be used. For example, megohmmeter measurements are an appropriate alternative to the procedure described below for measuring isolation resistance. Well-established calculation methods also exist to determine electrical energy on high voltage buses. / The following procedures should be performed after each of the specified crash tests.	附件11 / 電力安全性-測試程序 / 導電安全性測試方法(本項為新增之附件)：除本附件所述之測試方法外，亦可使用其他具相同效力之測試或分析方法。例如高阻器測量法即為一適當可代替下述絕緣電阻量測之方法。亦存在完善建立之計算分析方法可作為計算在高電壓匯流排電能之用。 / 應於碰撞測試後執行下述程序。
1 Test setup and equipment / If a high voltage disconnect function is used, measurements are taken from both sides of the device performing the disconnect function. / However, if the high voltage disconnect is integral to the RESS or the energy conversion system and the high-voltage bus of the RESS or the energy conversion system is fully enclosed within a physical barrier or enclosure that maintains protection class IPXXB after crash test, measurements may be taken only downstream of the device performing the disconnect function. / The voltmeter used in this test shall measure DC values and have an internal resistance of at least 10 mega ohms.	1. 測試整備及儀器設備 / 假如高電壓斷開功能被使用，量測值的取得是由兩造雙方裝置所造成之電壓斷開功能下取得。 / 然而，假如高電壓斷開是充能系統或能量轉換系統和充能系統的高電壓匯流排或在能量轉換系統是全部擁有在碰撞測後仍保持有IPXXB防護等級之物理屏障或外殼，量測值的取得僅從該裝置斷開功能表現的下游取得。 / 電壓計使用於本測試應量測直流的數值和內部阻抗至少10兆歐姆。
2 Bus voltage / The following instructions may be used if voltage is measured. / Prior to the vehicle crash test measure and record the high voltage bus voltage (Vb) (see Figure 1 ). If Vb is high voltage, conduct the specified vehicle crash test. After the crash test, determine the high voltage bus voltages (Vb, V1, V2) (see Figure 1). If the RESS has exposed conductive parts, measure the voltage V3 between any exposed conductive parts of it and the electrical chassis. / The measurement shall be made after 5 seconds (Test difficult to perform) of the vehicle coming to rest after each crash test.	2.匯流排電壓 / 下述的指示適用於電壓的量測。 / 在車輛碰撞量測之前後記錄高電壓匯流排電壓(Vb)（如圖一）。假如(Vb)是高電壓，進行指定的車輛碰撞測試。在經過碰撞測試後，決定高電壓匯流排電壓(Vb, V1, V2) （如圖一）。假如充能系統暴露可導電元件，在它的任意暴露可導電元件和電路介面中測量V3之電壓。 / 量測結果應在車輛每次做完碰撞試驗後的5秒後（測試難以執行）取得。
V3 is not used in the text ? To discuss the test during the meeting
3 Resistance isolation / The following instructions may be used if isolation resistance is measured. / Before the vehicle crash test, measure and record the high voltage bus voltage (Vb) (see Figure 1). Vb must be equal to or greater than the nominal operating voltage as defined by the vehicle manufacturer. / It is acceptable for vehicle manufacturer to elect to calculate or simulate this value instead of measuring this after the crash. / Measure and record the voltage (Vb) between the negative and the positive side of the high voltage bus (see Figure 1): / Measure and record the voltage (V1) between the negative side of the high voltage bus and the electrical chassis (see Figure 1): / Measure and record the voltage (V2) between the positive side of the high voltage bus and the electrical chassis (see Figure 1): / If V1 is greater than or equal to V2, insert a standard known resistance (Ro) between the negative side of the high voltage bus and the electrical chassis. With Ro installed, measure the voltage (V1’) between the negative side of the high voltage bus and the vehicle electrical chassis (see Figure 2). Calculate the isolation resistance (Ri) according to the formula shown. Divide this electrical isolation resistance value (in ohms) by the working voltage of the high voltage bus (in volts). / Ri = Ro*(Vb/V1’ – Vb/V1) or Ri = Ro*Vb*(1/V1’ – 1/V1)	3. 絕緣電阻 / 在絕緣電阻是可量測的情形下，下述的指示是可被使用的。 / 在執行車輛碰撞測試之前，測量和紀錄高壓匯流排的電壓(Vb)（如圖一）。Vb應等同或車輛製造廠規範之大於標稱工作電壓。 / 適用於車輛製造廠來選擇計算或模擬數值取代碰撞測試後的量測。 / 電壓(Vb)的量測和記錄在高電壓匯流排的陰極和正極之間（如圖一）： / 電壓(V1)的量測和記錄在高壓匯流排的正極和電路介面之間（如圖一）： / 電壓(V2)的量測和記錄在高壓匯流排的正極和電路介面之間（如圖一）： / 假如V1大於或等於V2，輸入一標準已知之電阻（Ro）在高壓匯流排的負極和電路介面之間。隨著Ro的輸入，量測負極的高電壓匯流排和電路介面之間的電壓(V1’)（如圖二）。絕緣電阻(Ri)的計算是根據公式所得的。 / 絕緣電阻（歐姆）除以高電壓匯流排（伏特）的工作電壓。 / Ri = Ro*(Vb/V1’ – Vb/V1) / or Ri = Ro*Vb*(1/V1’ – 1/V1)

If V2 is greater than V1, insert a standard known resistance (Ro) between the positive side of the high voltage bus and the electrical chassis. With Ro installed, measure the voltage (V2’) between the positive side of the high voltage bus and the electrical chassis (See Figure 3). / Calculate the isolation resistance (Ri) according to the formula shown. Divide this electrical isolation value (in ohms) by the working voltage of the high voltage bus (in volts). / Ri = Ro*(Vb/V2’ – Vb/V2) / or Ri = Ro*Vb*(1/V2’ – 1/V2)	假如V2大於V1，輸入一標準已知的阻抗（Ro）在高壓匯流排之正極和電路介面。隨著Ro的輸入，量測正極的高電壓匯流排和電路介面之間的電壓(V2’)（如圖三）。 / 絕緣電阻(Ri)的計算是根據公式所得的。絕緣電阻（歐姆）除以高電壓匯流排（伏特）的工作電壓。 / Ri = Ro*(Vb/V2’ – Vb/V2) / or Ri = Ro*Vb*(1/V2’ – 1/V2)

NOTE 1: The standard known resistance Ro (in ohms) should be approximately 500 times the working voltage of the vehicle (in volts). Ro is not required to be precisely this value since the equations are valid for any Ro; however, an Ro value in this range should provide good resolution for the voltage measurements.	備註1：這標準已知的阻抗Ro（歐姆）應接近車輛工作電壓（伏特）的500倍。自從這方程式能求得Ro值後，Ro就沒有必要用精準的數值，然而，Ro的數值在這一範圍內應提供對電壓測量一個好的解決方式。
4 Electrical Energy / The following procedure may be used if energy is measured. / After the vehicle crash determine the high voltage bus energy (see Figure 4). Install switch S1 and known resistance Re. Close switch S1 and measure and record voltage Vb and current Ie. Integrate the product of these two measurements with respect to time as shown below to obtain total energy.	4. 電能 / 下述的程序的使用適用於能量的量測。 / 經過車輛的碰撞來決定高電壓匯流排的能量（如圖4）。輸入在S1開關及已知阻抗Re上。接近S1開關、量測及紀錄Vb電壓和電流Ie. 整合這兩種對時間量測的產品如下述包含全部之能量。

5 Physical Barrier / The following procedure may be used if physical protection is tested. / 5-1 Test conditions / The manufacturer shall define the barrier,enclosure and solid insulator that protect / the human from the direct contact to the highvoltage bus in use (hereinafter referred to as the ‘original physical protection’). / Any surrounding parts of the high voltage components that can be opened, disassembled or removed without the use of tools after crash test shall be opened, disassembled or removed. / Surrounding parts that cannot be opened, disassembled or removed without the use of / tools are considered as a part of the physical barrier. / The access probe is pushed against any openings of the physical barrier with the force specified in table 1 - table 1 to be defined If it partly or fully penetrates into the original physical protection, it is placed in every possible position. / Starting from the straight position, both joints of the test finger shall be successively bent through an angle of up to 90 degree with respect to the axis of the adjoining section of the finger and shall be placed in every possible position.	5. 物理阻隔 / 下述程序的使用適用於測試物理的保護。 / 5-1測試條件 / 製造廠應該定義阻隔、外殼和固體絕緣體，用來阻隔防護當高電壓匯流排正在運作中人們之直接接觸。（以下簡稱為”原始之物理保護”） / 周圍任何地方的高壓元件可以打開，拆卸或移除不再使用的工具，在碰撞測試後，應當立即開始，拆卸或移除。 / 周邊部件，無法打開，拆卸或移除不再使用的工具，被認為是物理阻隔的一部份。 / 接觸棒以力量推擠物理阻隔的任何開口，規範於表一所示，表一是用來定義假使部分或全部穿入到原始物理保護，它被放置在一切可能的位置。 / 從直的地點開始，兩者測試棒的接頭應連續彎曲通過一角度大於90度將測試棒的相鄰區間的軸和應置於每一可能之位置。
5-2 Acceptance conditions / The access probe shall not touch live parts. / A mirror or a fiberscope may be used in order to inspect whether the access probe touches the high voltage buses, if necessary.	5-2可接受條件 / 接觸棒應無碰觸帶電體。 / 如有必要，鏡子或纖維鏡可用於以檢查接觸棒是否觸及高電壓匯流排。
Annex 11 – Appendix 1 - Protection degrees	附件11-附錄1-保護等級

The jointed test finger may penetrate over its full length of 80 mm but shall not contact the hazardous parts, even when its joints are bent at any optional angle (up to 90° from its axis) and are brought into any possible position. The stop face (Ø50 mm _20 mm) shall not pass through the opening. / The test force shall be 10 N _10 %.	接觸棒的接頭穿過長度80公釐但沒接觸到危險零件，即使當它的接頭彎曲在任何可選擇的角度（從它的軸大於90度）和帶入任何可能之位置。末端(Ø50 mm ± 20 mm)應不會通過開口。 / 測試所施之力應為10 N ± 10 %.

The rigid test wire (diameter 1,0 mm, 100 mm long) may penetrate over its full length of 100 mm, but shall be sufficiently distant from hazardous parts in any possible angular position. / The stop face (sphere Ø35 mm) shall not pass through the opening. / The test force shall be 1 N _10 %.	堅硬的試驗線（直徑1,0公釐，100公釐長）可能會穿透全長100公釐，但應完全遠離在任何可能角度位置之危險零件。 / 但應充分遠離危險地區，在任何可能的角位置。 / 末端(sphere Ø35 mm)應不會通過開口。 / 測試所施之力應為1 N ± 10 %.